# EDDYNET PICK UP / ANGLE SWEEPER
(FLEXX-24’’ OR 32’’)

- The FLEXX-24’’ or 32’’ sweeps when being pushed

- Hydraulic drive

- Brush diameter 24’’ or 32’’

- The FLEXX-24’’ or 32’’ model is recommended to be installed on loader arm of tractor or backhoe

General

- Pick up & angulation sweeper, to be installed on a loader arm of

tractor or backhoe

- The sweeper has a brush flotation system allowing it to follow the

variations of the road

- Pivoting quick coupler front/rear, left/right and 6’’ up/down slide

- The brush is supported by two ball bearings

- 4 anchor rings for handling and transportation

- Rubber travelling springs

- Adjustement of the brush pressure, on the ground, with two

shock absorbers

Brush Drive

- Requires a minimum of 12 GPM at 2000 PSI

- The brush is driven by one hydraulic motor mounted directly on

the center core

- Motor driven by the hydraulic system of the carrier machine and

controlled by the sweepers valve block

- The hydraulic holes from the pump to the third valve must be ¾’’

in diameter

- Hydraulic valve block to supply the brush, the opening of the

hopper (bucket), angulation, gutter brush and lifting (optional)

Brush (model FLEXX-24)

- Replaceable disc brush, exterior diameter 24’’ with a 6 3/8’’ interior diameter (core).

- Choice of brushes: polypropylene only or polypropylene/wire

Brush (model FLEXX-32)

- Replaceable disc brush, exterior diameter 32’’ with a 10’’ interior diameter (core).

- Choice of brushes: polypropylene only or polypropylene/wire

Hydraulic Angulation (25 degrees)

- Hydraulic angulation of 25( on each side

Pick up hopper (bucket)

- Lifting of the hopper 4’’ off the ground when sweeping left/right

- Pivoting of the hopper (bucket) by two hydraulic cylinders

- Hardened steel runners under the hopper for protection

Structure

- Laser cut parts for a better design and smoother finish

- Tubular structure, robust construction

- 16 gauge steel hood, covering 180(  of the brush

Finish

- Powder coat

- All parts are painted individually

Pivoting wheels

- 2 or 4 load bearing wheels 4’’ x 8’’ no maintenance required

Various

- 6 function electric solenoid valve

- Gutter brush (6 sections) with independent hydraulic lift function

- Hydraulic selector for gutter brush

- Electric hydraulic valve block to power the brush, opening / close

the hopper, sweeper angulation right / left, move up / down and

start  the gutter brush

hopper and angulation if only one flow control is provided on the

carrier machine

- Wireless remote control

# Text boxes

Standard features

Standard features

Options